## Slide 1: Instruction Execution and Sequencing

## Slide 2: Outline
Instruction Execution procedure
Instruction Sequencing
  Straight Line Sequencing
  Branching
Subroutines
  Call and Return mechanism
  Subroutine Linkage method

## Slide 3
A program for c ←[A]+[B]

## Slide 4: Instruction execution…
It is a Two phase procedure :
  Instruction Fetch
  Instruction Execution
‘i’ is placed into the PC
the processor control circuits use the information in the PC to fetch instructions, one at a time.
Fetching is in the order of increasing addresses and is called straight-line sequencing
Then the execution of the instruction proceeds by transferring the instruction pointed by PC into Instruction Register (IR).
During instruction execution, PC is incremented by 4 ,i+4, i+8,i+12,..

## Slide 5: Branching
Fig: Straight line program to add numbers

## Slide 6: Branching…
Fig: Using Loop to add numbers
Placing single ‘ADD’ instruction in a loop
Loop Executed many times
Register R1 used as counter
BRANCH instruction: it loads a new value called
branch target into program counter.
Fetching and execution happens with new address.

## Slide 7: Condition Codes
N (negative)
Z (zero)
V (overflow)
C (carry)

## Slide 9: Status

## Slide 10: SUBROUTINES and CALL

## Slide 11: Subroutines
Particular subtasks performed (many times) using different data values.
Program branches to a subroutine: calling a subroutine (CALL instruction)
By executing ‘RET’ (return instruction); it returns to the main program.
CALL- RET mechanism is ‘SUBROUTINE LINKAGE METHOD’
Link register- saves the return address at specified location

## Slide 14: Subroutines