## Slide 1: Module 1 – introduction to 8086

## Slide 2: Architecture of 8086
Source: https://www.includehelp.com/embedded-system/architecture-of-8086-microprocessor.aspx as on 17 July 2020

## Slide 3: Memory segmentation
To increase the fetching speed and the execution speed, the memory is segmented in 8086
20 bit address bus can address 1MB of memory
It is divided into 4-64kB segments
Thus, among 1 MB memory, 8086 uses only 4 64kB segments

## Slide 4: Internal architecture
Internal architecture of 8086
Bus Interface Unit (BIU)
Execution Unit

## Slide 5: 1. Bus interface unit (BIU)
System bus is used to provide interface between the system memory and I/O devices
Performs various jobs such as memory read, I/O read etc.

## Slide 6: Functions of BIU
Generates 20 bit physical address for accessing memory
Obtains instructions from memory
Transfers data from and to the I/O and memory
Pipelining – fetches 6 instructions in prior
BIU contains
  4 Segment registers
  Instruction Pointer
  Address Generation Circuit

## Slide 7: Instruction Pointer
16 bit registers
Holds the offset of the next instructions in the code segment
It is incremented after every instruction byte is obtained
Address of net instruction is calculated as CSx10H+IP

## Slide 8: Registers
Code segment register – Holds the base address of the code segment. Every program is stored in the CS and each instruction is accessed with the help of instruction pointer
Data Segment register – Holds the base address for data segment
Stack segment register – Holds the base address for stack segment
Extra segment register - Holds the base address of the extra segment

## Slide 9: Address generation
BIU generates the address
Generates 20 bit address using segment and offset addresses
Segment address x 10H + Offset Address

## Slide 10: 6 byte prefetch queue
It is a 6 byte queue (FIFO)
Fetches the next instruction when executing the current instruction – pipelining
Erased whenever a branch instruction occurs

## Slide 11: 2. Execution unit
Main components
  General purpose registers
  ALU
  Special Purpose registers
  Instruction register
  Instruction decoder
  Flag/status register

## Slide 12: Functions
Obtains instructions form the queue in BIU, decodes them and performs arithmetic and logical operation using ALU
Sends control signals for internal data transfer
Sends request signals for accessing I/O devices
Operates with respect to clock cycles

## Slide 13: General Purpose registers
4 16 bit general purpose registers
AX register – holds operands during arithmetic operations. Used as accumulator during string operations
BX register – Holds the memory address (offset)
CX register – holds count for instructions such as loop, rotation, shifting, string operations etc.
DX register – Used with AX register to hold a total of 32 bit value during multiplication and division

## Slide 14: Arithmetic and Logical unit
Performs 8 and 16 bit arithmetic operations

## Slide 15: Special purpose registers
Stack pointer – points to the top of the stack. Used during PUSH, POP, CALL etc.
Base Pointer – Holds the Offset address of any location in the stack segment. To access random locations in the stack.
Source Index – Holds offset address in data segment during string operations
Destination index – Holds the offset address in the Extra segment during string operations

## Slide 16: Flags/Status register
6 Status Flags
  Carry Flag
  Parity Flag
  Auxiliary carry flag
  zero flag
  Sign flag
  Overflow flag
3 Control Flags
  Trap Flag
  Interrupt Flag
  Direction Flag

## Slide 17: weblinks
https://www.geeksforgeeks.org/architecture-of-8086/
https://www.tutorialspoint.com/microprocessor/microprocessor_8086_overview.htm#:~:text=8086%20Microprocessor%20is%20an%20enhanced,like%20multiplication%20and%20division%20easily.
https://stackoverflow.com/questions/36442060/why-is-any-value-saved-in-a-segment-register-multiplied-by-10