## Slide 1: Module 2: Introduction to ALP
Dr. P. Nirmala
Assistant Professor (SG – 1)
SENSE, VIT

## Slide 2: ALP – Assembly Language Programming
Low level programming language that is specific for a particular computer architecture.
What is an assembler?
  A code that converts the basic computer instructions into bits that the computer can understand
  To access, operate and manage hardware in the computer architecture

## Slide 3: Assembler Directives of 8086 microprocessor
Assembler directives are instructions that instructs the assembler to do some specific task
For e.g., the directive might prompt the assembler to allocate memory for a variable, to include source file, etc.

## Slide 4
The DB directive
The DW directive
The DD directive
The STRUCT (or STRUC) and ENDS directives
The EQU Directive
ASSUME
EXTERN
GLOBAL
SEGMENT
PROC
GROUP
NAME
INCLUDE

## Slide 5
DB
The DB directive is used to declare a BYTE type variable – A BYTE is made up of 8 bits.
Declaration examples:
Byte1 DB 10h
Byte2 DB 255 ; 0FFh, the max. possible for a BYTE
DW
The DW directive is used to declare a WORD type variable – A WORD occupies 16 bits or (2 BYTE).
Declaration examples:
Word DW 1234h
Word2 DW 65535; 0FFFFh, (the max. possible for a WORD)

## Slide 6
DD
The DD directive is used to declare a DWORD – double word is made up of 32 bits =2 Word’s or 4 BYTE.
Declaration examples:
Dword1 DW 12345678h
Dword2 DW 4294967295 ;0FFFFFFFFh.
STRUCT and ENDS
STRUCT and ENDS directives to define a structure template in order to group data items.
The STRUCT directive tells the assembler that a user defined uninitialized data structure follows.
A structure element is referenced with the base “+” operator before the element’s name.
A Structure ends by using the ENDS directive meaning END of Structure.

## Slide 7
Syntax
  STRUCT/STRUC
  Struct_ele_name ele_data type?
  ..
  ..
  ENDS
  E.g.,
  STRUCT
  BYTE1 DB?
  BYTE2 DB?
  WORD1 DW?
  DWORD1 DW?
  ENDS

## Slide 8: EQU
The EQU directive is used to assign a name to some value or symbol.
Each time the assembler finds the given names in the program, it will replace the name with the value or a symbol.
The value can be in the range 0 through 65535
The following operators can also be used to declare an Equate:
  THIS BYTE
  THIS WORD
  THIS DWORD
But an Equate does not have an address or space reserved for it in the .COM file.

## Slide 9: Example
FAC EQU 04H ;
Write this statement at the beginning of your program and later in the program you can use this as follows:
ADD AL, FAC

## Slide 10: ASSUME
It tells the assemble what name must it assume for a specified logical segment
E.g,
ASSUME CS: CODE
  This indicates the assembler that the instructions are present in the CODE segment
ASSUME DS

## Slide 11: EXTRN
It is used to tell the assembler that the name or label following the directive are some other assembly module
Eg.,
  EXTRN SMART-DIVIDE: FAR

## Slide 12: GLOBAL
GLOBAL directive is used to make the symbol available to the other modules. Example:
GLOBAL DIVISOR:
tells the assembler that DIVISOR is a variable of type of word which is in another assembly module.

## Slide 13: SEGMENT
It is used to indicate the start of a logical segment. It is the name given to the segment. Example: the code segment is used to indicate to the assembler the start of logical segment.
PROC: (Procedure)
It is used to identify the start of a procedure. It follows a name we give the procedure.
After the procedure the term NEAR and FAR is used to specify the procedure
Example: SMART-DIVIDE PROC FAR identifies the start of procedure named SMART-DIVIDE and tells the assembler that the procedure is far.

## Slide 14: NAME
It is used to give a specific name to each assembly module when program consists of several modules.
Example: PC-BOARD – Instructions for printed circuit boards
INCLUDE
It is used to tell the assembler to insert a block of source code from the named file into the current source module.

## Slide 15
It can be used to tell the assembler to group the logical segments named after the directive into one logical group. This allows the contents of all he segments to be accessed from the same group.
Example: SMALL-SYSTEM GROUP CODE, DATA, STACK-SEG.
GROUP

## Slide 16: Weblinks
http://www.sakshieducation.com/Story.aspx?nid=93723
https://nptel.ac.in/content/storage2/courses/106108100/pdf/Teacher_Slides/mod2/M2L2.pdf
https://www.docsity.com/en/assembler-directive-of-8086/4105338/