## Slide 1: Module 2: Introduction to ALP
Dr. P. Nirmala
Assistant Professor (SG – 1)
SENSE, VIT

## Slide 2: Assembly Language programming
If then else
For loop
While loop

## Slide 3: Jump inst..
jmp <label> - unconditional jump to a given address
jz <label> - jump if the zero flag has been set (because some operation returned a Zero result)
jnz <label> - jump if the zero flag is not set
je <label> - jump of the equality flag is set (typically the result of comparing two values)
jne <label> - jump if the equality flag is not set

## Slide 4: If Then Else
Syntax:
if:
; comparison statement
; if body statements
; if comparison is false, goto else
jmp endif
else:
; else statements
;
endif:

## Slide 5: IF Then Else
if AX < BX {part_1} else {part_2}
where AX and BX are signed integers, in all x86 you would:
CMP AX,BX ; comparing AX with BX JL label1 ; jump if AX is LESS than BX ; do part_2 stuff JMP SHORT label2 ; finished part_2 jump forward to label2
label1: ; do part_1 stuff ; finished label2:

## Slide 6: For Loop
Syntax:
for(int x = 0; x<=3; x++)
{
Instruction 1;
Instruction 2
.
.
.
Instruction n;
}

## Slide 7: For loop in 8086
Example:
MOV CX,0 cx register is set to 0
Loop1: Instructions All the instructions are here, should not change cx
INC CX Increment
CMP CX,3 Compare cx to the maximum iteration value, here 3
JLE loop1 Goto Loop until less or equal to 3
JLE -Jump short if less or equal

## Slide 8
For example, if we wish to do a certain job for 4 times, and we do not want to change the index, then we can use
mov cx, 4 i.e., 4 iterations
Loop1: Instructions Whatever you want do goes here, it should not change cx
loop loop1 loop instruction decrements cx and jumps to label if not 0
If there is a very simple instruction to be completed for a constant number of times, then we can use an assembler directive to hardcore that instruction. For example,
Times 4 Instruction DO that instructions 4 times.

## Slide 9: Example..
Example Program:
LXI D,45 00 Load destination address in DE pair
LXI H,4100 Load the count in HL pair
MOV C,M Copy the count to register C
LOOP INX H Increment memory
MOV A,M Copy element to Accumulator
STAX D Store the element to the address in the DE pair
INX D Increment destination address
DCR C Decrement count
JNZ LOOP Jump on non-zero to the label LOOP
HLT Program ends

## Slide 10: While loop
While (x==1)
{
Instructions
…
…
}

## Slide 11: While loop in ALP
JMP loop1 Jump to condition first
Cloop1: Instruction Execute the content of the loop
Loop1: CMP AX,1 Check the condition
JE cloop1 Jump to content of the loop if met
(JE- Jump if it is equal)

## Slide 12: Weblinks
https://www.youtube.com/watch?v=4ARCKQpOHLk
https://www.tutorialspoint.com/assembly_programming/assembly_loops.htm
https://www.youtube.com/watch?v=9do0dyEHF2M
http://www.vpscience.org/materials/US06CCSC04_4.pdf