## Slide 1: Module 3: Advanced ALP
Dr. P. Nirmala
Assistant Professor (SG – 1)
SENSE, VIT

## Slide 2: Interrupt programming using DOS BIOS function calls

## Slide 3: What are interrupts?
What would you do when you get a WhatsApp message when you are listening to a lecture?
Which interrupt would you choose?
  Knock on the door or a phone call?
  Interrupts have priority
  Some interrupts are more important than the other

## Slide 4: Introduction to interrupts
They cause temporary stop in the execution of the program
When the microprocessor is executing some program, an interrupt breaks the sequence and diverts the sequence to some other program called Interrupt Service Routine (ISR)
Once the ISR is tended to, the control is then returned to the main program

## Slide 5: Interrupt sources
Interrupts are needed to connect peripheral devices that have lower data rate than the CPU.
An external signal applied  Hardware interrupt
Interrupt instruction  Software interrupt
Interrupt due to error condition

## Slide 6: Interrupt Process
Keyboard Controller

## Slide 7: DOS and BIOS interrupts
Application program
DOS Support
BIOS Support
I/O peripheral Devices

## Slide 8: DOS Interrupts
When MS-DOS is loaded in the computer INT 21H is used to provide an interrupt to perform some important functions.
These are called DOS INT 21H function calls.
Main function calls are data input/output through keyboard
Example:
MOV AH, 01  to input one character
INT 21H  invoke interrupt

## Slide 9: DOS (Disk Operating System) Interrupts
Function Call 01  Read the keyboard
  Input parameter AH = 01  Read a character from keyboard
Function Call 02  Display on CRT screen
  Input parameter AH = 02  ASCII character to be displayed in the screen
Function Call 03  Read character from COM 1

## Slide 10: DOS Interrupt continued
Function Call 04  Write character to COM 1
Function Call 05  Write to printer attached to Lpt1
Function Call 09  Display a character string
Function call 0ah  Buffer keyboard input

## Slide 11: BIOS Interrupts
The INT 10H subroutines are burned into the ROM BIOS of the 8086 and the compatible hardware and instructions are used to communicate with the user through the screen.
Example  changing colors of characters, background, changing cursor locations, clearing screen.

## Slide 12: Difference between DOS and BIOS
BIOS is a firmware that is burnt in ROM and it starts its work on Start up of the processor
It checks whether every hardware connected to the system is proper at the time of booting
For example, it would accommodate date and time settings, keyboard, DVD etc.
It is present in the motherboard of the CPU
DOS is Disk Operating System which is the actual OS present in the hard drive initially.
While starting the computer, the BIOS checks for all the components connected to the computer, and if they are all fine, then it would make the OS get loaded in RAM for starting it.

## Slide 13: BIOS (Basic Input/Output System) Interrupts
Function Call 00 – Select Video mode
  Here Al  mode Number, Ah = 00
  Al = 00  40 x 25 black and white
  Al = 04  320 x 200 colour
  Al = 10H  640 x 350 x 16 colour
Function call 03  Read cursor position
  Ah = 03, Bh = Page number (Input Parameters)

## Slide 14: BIOS Interrupts Continued
Function call 0E  Write character on CRT screen and advance cursor
INT 11H  Determine the type of equipment installed
INT 14H  To control the serial communication port attached to the computer
INT 16H  Keyboard interrupt

## Slide 15: Weblinks
http://www.ablmcc.edu.hk/~scy/CIT/8086_bios_and_dos_interrupts.htm
https://www.slideshare.net/VijayKumar486/8086-interrupts-with-dos-and-bios-by-vijay/60
http://www.ece.lsu.edu/desouza/Classes/EE3751/Lab%203.pdf
http://faculty.uml.edu/yluo/teaching/microprocessorii/resources/interrupts.pdf