## Slide 1: Module 3: Advanced ALP
Dr. P. Nirmala
Assistant Professor (SG – 1)
SENSE, VIT

## Slide 2: File Management using MS DOS
File management is very important as far as an operating system (OS) is concerned because it is responsible for creation, storage, changing and deletion of important files and file systems.
The disk operating system (DOS) takes care of the file management in any OS.
Let us see some of the file management procedures that Microsoft DOS (MS DOS) handles.

## Slide 3: 1. Open file
Open File Function (ah): 3Dh
Entry parameters:
al- file access value
0- File opened for reading
1- File opened for writing
2- File opened for reading and writing
ds:dx- Point at a zero terminated string containing the filename.
Exit parameters: If the carry is set, ax contains one of the following error codes:
2- File not found
4- Too many open files
5- Access denied
12- Invalid access

## Slide 4: 2. Create file
Function (ah): 3Ch
Entry parameters:
ds:dx- Address of zero terminated pathname
cx- File attribute
Exit parameters: If the carry is set, ax contains one of the following error codes:
3- Path not found
4- Too many open files
5- Access denied

## Slide 5: Cont..
There is another parameter passed in cx called the initial file attribute settings. The six bits of cx contain the following values:
Bit - Meaning if equal to one
0 - File is a Read-Only file
1 - File is a hidden file
2 - File is a system file
3 - File is a volume label name
4 - File is a subdirectory
5 - File has been archived

## Slide 6: 3. Close file
Function (ah): 3Eh
Entry parameters: bx- File Handle
Exit parameters: If the carry flag is set, ax contains 6, the only possible error, which is an invalid handle error.

## Slide 7: 4. Read from a file
Function (ah): 3Fh
Entry parameters: bx- File handle
cx- Number of bytes to read
ds:dx- Array large enough to hold bytes read
Exit parameters: If the carry flag is set, ax contains one of the following error codes
5- Access denied
6- Invalid handle If the carry flag is clear, ax contains the number of bytes actually read from the file.

## Slide 8: 5. Write to file
unction (ah): 40h
Entry parameters: bx- File handle
cx- Number of bytes to write
ds:dx- Address of buffer containing data to write
Exit parameters: If the carry is set, ax contains one of the following error codes
5- Accessed denied
6- Invalid handle

## Slide 9: 6. Set disk transfer address (DTA)
Function (ah): 1Ah
Entry parameters: ds:dx- Pointer to DTA
Exit parameters: None

## Slide 10: 7. Find first file
Function (ah): 4Eh
Entry parameters: cx- Attributes
ds:dx- Pointer to filename
Exit parameters: If carry is set, ax contains one of the following error codes
2- File not found
18- No more files

## Slide 11: 8. Find next file
Function (ah): 4Fh
Entry parameters: none
Exit parameters: If the carry is set, then there aren’t any more files and ax will be returned containing 18.

## Slide 12: 9. Delete file
Function (ah): 41h
Entry parameters: ds:dx- Address of pathname to delete
Exit parameters: If carry set, ax contains one of the following error codes
1 File not found
5- Access denied

## Slide 13: 10. Rename file
Function (ah): 56h
Entry parameters:ds:dx- Pointer to pathname of existing file
es:di- Pointer to new pathname
Exit parameters: If carry set, ax contains one of the following error codes
2- File not found
5- Access denied
17- Not the same device

## Slide 14: 11. change/get file
Function (ah): 43h
Entry parameters: al- Subfunction code
1 Return file attributes in cx
2 Set file attributes to those in cx cx- Attribute to be set if AL=01
ds:dx- address of pathname
Exit parameters: If carry set, ax contains one of the following error codes:
1 Invalid function
2 Pathname not found
Access denied

## Slide 15: 12. Get/Set File Date and Time
Function (ah): 57h
Entry parameters: al- Subfunction code
1 Get date and time
2 Set date and time
bx- File handle
cx- Time to be set (if AL=01)
dx- Date to be set (if AL=01)
Exit parameters: If carry set, ax contains one of the following error codes
1 Invalid subfunction
2 Invalid handle

## Slide 16: weblinks
http://www.hermit.cc/it/dos/dosstruc.htm
https://www.plantation-productions.com/Webster/www.artofasm.com/DOS/pdf/ch13.pdf
https://www.youtube.com/watch?v=Ck_EsnVvHdM&t=3s