## Slide 1: Module 3: Advanced ALP

## Slide 2: What are interrupts?
What would you do when you get a WhatsApp message when you are listening to a lecture?
Which interrupt would you choose?
  Knock on the door or a phone call?
  Interrupts have priority
  Some interrupts are more important than the other

## Slide 3: Definition of Interrupts
Used to break the sequence of operation.
While the CPU is executing a program, an ‘interrupt’ breaks the normal sequence of execution of instructions, diverts its execution to some other program called Interrupt Service Routine(ISR).
After executing ISR , the control is transferred back again to the main program.

## Slide 4: Need for Interrupt
Interrupts are particularly useful when interfacing I/O devices that provide or require data at relatively low data transfer rate.

## Slide 5: Sources of Interrupts in 8086
.
An external signal applied to NMI or INTR input Pin Hardware interrupt
Execution of Interrupt instruction  Software interrupt
Interrupt due to error condition produced in 8086 instruction execution process (divide by zero, overflow errors)

## Slide 6: Hardware Interrupts(External interrupt)
caused by any peripheral device by sending a signal through a specified pin to the microprocessor.
Two hardware interrupt pins: INTR and NMI. One more interrupt pin associated is INTA called interrupt acknowledge
Interrupt
Hardware interrupt
Maskable interrupt
Non maskable interrupt

## Slide 7: Hardware Interrupts(External interrupt)
NMI- Non Maskable Interrupt
Any interrupt request at NMI input cannot be masked/disabled by any means.
higher priority than the maskable interrupt request pin (INTR) and it is of type 2 interrupt.
INTR- Maskable Interrupt
It is a maskable interrupt, because it will be masked using Interrupt flag(IF).
Activated by an I/O port.

## Slide 8: Software interrupts
Inserted at the desired position into the program to create interrupts.
INT- Interrupt instruction with type number.
INTR is of 256 types and it may be from 00 to FFH or (00 to 255)

## Slide 9: INTERRUPT VECTOR TABLE
It is crucial to an understanding of hardware and software interrupts.
Reserved 1024 loactions for storing the interrupt vector table.
8086 supports 256 type of interrupts.(00 to FFH).
Each interrupt need 4 bytes. i.e 2 bytes each for IP and CS of its ISR
Int type x 4= gives offset address in Zeroth code segment at which IP and CS addresses of ISR are stored.

## Slide 10
TYPE 0 :
The divide error whenever the result from a division overflows or an attempt is made to divide by zero.
ISR is responsible for displaying the message “Divide Error” on the screen
INT 01
Single step or trap occur if the trap flag is set to 1.
Upon accepting this interrupt, the TF bit is cleared so that the interrupt service procedure executes at full speed.

## Slide 11
TYPE 2
Non-maskable interrupt occurs when a logic 1 is placed on the NMI input pin to the microprocessor.
This input is non-maskable, which means that it cannot be disabled.
TYPE 3 :
A special one-byte instruction (INT 3) that uses this vector to access its interrupt service procedure.
The INT 3 instruction is often used to store a breakpoint in a program for debugging.
TYPE 4:
Overflow is a special vector used with the INTO instruction.
The INTO instruction interrupts the program if an overflow condition exists, as reflected by the overflow flag (OF).

## Slide 12: PRIORITY OF INTERRUPTS

## Slide 13: Steps involved in processing an interrupt instruction by the processor

## Slide 14: INTERRUPT PROGRAMMING

## Slide 15: DOS and BIOS interrupts
Used to perform some very useful functions, such as displaying data to monitor, reading data from keyboard.
Used by identifying the interrupt option type, which is the value stored in register AH.

## Slide 16: DOS Interrupts 21H
When MS-DOS is loaded in the computer INT 21H is used to provide an interrupt to perform some important functions.
These are called DOS INT 21H function calls.
Main function calls are data input/output through keyboard
Example:
Option 1- Input a single character from keyboard
Register used:
AH=1
AL= the character inputted from keyboard
Ex:
MOV AH, 01 – option to input one character
INT 21H -invoke interrupt

## Slide 17: DOS Interrupts 21H
Option 2- output a single character to the monitor
Register used:
AH =2
DL = character to be displayed
EX:
MOV AH, 2
MOV DL, ‘A’
INT 21H

## Slide 18: DOS Interrupts 21H
Option 9: output a string of data terminated by $ to the monitor.
Register used:
AH=9
DX = offset address of data to be displayed
Ex:
MOV AH,09 ;option 9 to display string of data
MOV DX, OFFSET mess1
INT 21H ; invoke the interrupt

## Slide 19: DOS Interrupts 21H
Option 0AH: Input a string of data from the keyboard
Register used:
AH=0AH
DX = offset address of location where string will be stored
Ex:
.DATA
BUFFER1 DB 15,? 15 DUP(FF)
MOV AH,0AH ;
MOV DX, OFFSET Buffer1
INT 21H ;

## Slide 20: DOS Interrupts 21H
Option 4CH: Terminate a process, by returning control to a parent process or to DOS.
Register used:
AH=4CH
AL= binary return code
Ex:
MOV AH,4CH ;
INT 21H ;

## Slide 21: BIOS Interrupts
The INT 10H BIOS of the 8086 are used to communicate with the user through the screen.
Manipulation of screen text is done through INT 10H
Example  changing colors of characters, background, changing cursor locations, clearing screen.

## Slide 22: BIOS Interrupts 10H
It Controls The Video Display
Function Call 00: Select Video Mode
Input Parameter:
AH = 00H
AL = Mode Number
Function: It Changes The Display Mode And Clears The Screen
AL = 00 40 X 25 Black And White
AL = 04 320 X 200 Color
AL= 10H 640 X 350 X 16 Color

## Slide 23: BIOS Interrupts 10H
FUNCTION CALL 03: READ CURSOR POSITION
Input Parameter: AH = 03
BH = Page Number
Function: Reads Cursor Position On Screen
Output Parameters:
CH = Starting Line
CL = Ending Line
DH = Current Row
DL = Current Column

## Slide 24: BIOS Interrupts 10H
FUNCTION CALL 03: READ CURSOR POSITION
Input Parameter: AH = 03
BH = Page Number
Function: Reads Cursor Position On Screen
Output Parameters: CH = Starting Line
CL = Ending Line
DH = Current Row
DL = Current Column

## Slide 25: THANK YOU