## Slide 1: 8255 PERIPHERAL INTERFACING

## Slide 2: 8255
Parallel I/O port chip
Programmable peripheral I/O port
General purpose programmable I/O device
Designed for use with 8-bit, 16-bit and higher capability µP
Designed to interface the CPU with its outside world such as ADC, DAC, keyboard etc

## Slide 3: Internal Architecture

## Slide 4: Internal Architecture
24 I/O pins
Individually programmed in to
  Two groups of 12 lines each (Group A & Group B)
  Three groups of 8 lines each
Group A contains
  8-bit port (Port A) PA7 – PA0
  4-bit port (Port c upper) PC7 – PC4
Group B
  8-bit port (Port B) PB7 – PB0
  4-bit port (Port c lower) PC3 – PC0

## Slide 5: Internal Architecture
Port c upper and lower can be combined to function as 8-bit port
Three 8-bit I/O ports
Two 8-bit and two 4-bit I/O ports
All these ports can function independently either as input or output ports
  Programming the bits of an internal register (control word register – CWR)

## Slide 6: Internal Architecture
Three-state bi-directional 8-bit buffer is used to interface the 82C55 internal data bus with system data bus
Controlled by read/write control logic
Read/write control logic
  Manages all of the internal and external transfer of both data and control words
Data is transmitted or received by the buffer upon execution of input or output instructions by the CPU

## Slide 7: Signal Description
PA7-PA0
PB7-PB0
PC7-PC0
  Act as either latched output or buffered input
  Based on control word loaded into CWR
RD’
  Low
  Allows CPU to read from 8255
WR’
  Low
  Allows CPU to write data and control word in to 8255

## Slide 8: Signal Description (2)
CS’ (Chip select line)
  Low – enable 8255 respond to RD’ and WR’ signal
A1- A0
  Address input lines
  Driven by the microprocessor
  Used for addressing any one of four registers
    Three I/O ports and one CWR

## Slide 9: Signal Description (3)
D0-D7 (Data bus lines)
  Carry data or control word to/from µP
RESET
  High – Clears the control word register of 8255
  Initialize CWR to 9Bh
  All ports are set as input ports by default after reset

## Slide 10: Modes of Operation
I/O mode
  8255 work as programmable I/O ports
Bit Set-Reset (BSR) mode
  Only port C can be used to set or reset its individual port bits
I/O mode
  Mode 0 - Basic Input/Output
  Mode 1 - Strobed Input/Output
  Mode 2 - Bi-directional Bus

## Slide 11: BSR Mode
Any of the 8-bits of port C can be set or reset depending on B0 of control word
Bit to be set or reset is selected by bit select flags B3, B2 and B1 of the CWR

## Slide 12: BSR Mode Control Word Register Format

## Slide 13: I/O Mode CWR Format

## Slide 14: Mode 0
Basic input/output mode
Provides simple input and output capabilities using each of the three ports
Data can be simply read from and written to the input and output ports
1. Two 8-bit ports (port A and port B)and two 4-bit ports (port C upper and lower) are available
2. Any port can be used as an input or output port
3. Output ports are latched. Input ports are not latched
4. A maximum of four ports are available
  Overall 16 I/O configuration are possible

## Slide 15
CWR
Port address

## Slide 16
Interfacing
with 8086
IORD’ and IOWR’ readily available (8086 is in maximum mode)
Absolute decoding
All the 16 address lines for deriving the device address
A0 pin of 8086 is used for selecting the transfer on the lower byte of the data bus

## Slide 17: ALP
Get address of CWR in DX
Initialize CWR with 82H
Get address of port B in DX
Input port B value in to AL
Port B senses the switch position
Get address of port A in DX
Output AL value to port A
Initialize BL for switch count
Initialize CH for total number of switch

## Slide 18: Interfacing 16-bit 8255 ports with 8086. Address of port A is F0H
Two 8255 are required
One will act as the lower 8-bit port D0-D7
Other will act as upper 8-bit port D8-D15
No absolute decoding scheme
  Circuit is implemented using minimum hardware

## Slide 20: Matrix Keyboard Interfacing
Port address
  Port A – 8000H
  Port B – 8002H
  CWR – 8006H
Control word (CW) – 82H
8255 interfaced with lower byte of 8086 data bus
Absolute decoding is not used to implement the circuit using minimum hardware

## Slide 21: Key Debounce
Mechanical push button generate transient response whenever pressed/released
Microprocessor should wait for the transient period (10 ms)
Transient response settle down and reaches a steady state
8086 read logic zero when the key is pressed

## Slide 22: Identification of Key Pressed
Column identification
Row identification

## Slide 23: Column identification
Courtesy: OPENBOX Education

## Slide 24: Row Identification
Courtesy: OPENBOX Education

## Slide 25
Courtesy: OPENBOX Education

## Slide 26
Courtesy: OPENBOX Education

## Slide 27: ALP for Matrix Keyboard Interfacing
Load CW in to CWR

## Slide 28: ALP for Matrix Keyboard Interfacing
Load data to ground a row
Set row counter
Rotate AL to ground next row
Save data to ground next row
Output port (port A) address is in DX
Ground one of the row Let A0
Input port (port B) address is in DX
Read input port for key closure
Mask upper nibble of AL
Set column counter

## Slide 29: Procedure for Debouncing the Key

## Slide 31: Mode 1 (Strobed I/O mode)
Handshaking signal control, input or output function of the specified port
Port C is used for generating handshake (control) signal
  PC0-PC2 provide strobe or handshake lines for port B
  PC3-PC5 provide strobe or handshake lines for port A
Group B - Port B and PC0-PC2
Group A - Port A and PC3-PC5
Both inputs and outputs are latched
PC6 and PC7 may be used as independent data lines

## Slide 32: Mode 1 Control word Group Input A & B

## Slide 33: Input Control Signal Definition in Mode 1
STB’ (Strobe Input)
  LOW
  Data available at 8-bit input port is loaded into input latches
IBF (Input Buffer Full)
  Logic 1
  Data has been loaded into the latches (acknowledgement)
  Set by STB’
  Reset by rising edge of RD’

## Slide 34: Input Control Signal Definition in Mode 1
INTR (Interrupt Request)
  Set by a high at STB’ and high at IBF pin
  Reset by a falling edge on RD’ input
INTE (Internal flag)
  Controlled by BSR mode of PC4 (INTEA) or PC2 (INTEB)
External input device can request the service of the processor by putting the data on the bus and sending the strobe signal

## Slide 35: Mode 1 Strobed Input Data Transfer

## Slide 36: Output Control Signal Definition in Mode 1
OBF’ (output Buffer Full)
  LOW
  CPU written data to the specified output port
  Set by a rising edge of WR’
  Reset by falling edge at the ACK’ input
ACK’
  LOW
  Data transferred by CPU is received by the output device
INTR (Interrupt Request)
  Set when ACK’, OBF’ and INTE are 1
  Reset by falling edge on WR’

## Slide 37: Mode 1 Strobed Output Data Transfer

## Slide 38: Mode 1 Control word Group Output A & B

## Slide 41
https://www.youtube.com/watch?v=Q1I4-8fVShA
A.K. Ray and K.M. Bhurchandi Advanced Microprocessors and Peripherals, third Edition, Tata McGraw Hill, 2012.