## Slide 1: Module 6: Co-Processor

## Slide 2: Instruction Set
The mnemonics of the 8087 instruction begins with F so that there will not be any confusion between the instructions of microprocessor and the coprocessor.
F stands for floating point.
When an error condition occurs, the 8087 categorizes it as an ‘exception’ and sets the corresponding bit in the status register.
The 8087-instruction set can be categorized into four functional groups as follows:
DATA TRANSFER INSTRUCTIONS.
ARITHMETIC INSTRUCTIONS.
COMPARE INSTRUCTIONS.
TRANSCENDENTAL INSTRUCTIONS.

## Slide 3: I. Data Transfers Instructions
REAL TRANSFER
  FLD Load real
  FST Store real
  FSTP Store real and pop
  FXCH Exchange registers
INTEGER TRANSFER
  FILD Load integer
  FIST Store integer
  FISTP Store integer and pop
PACKED DECIMAL TRANSFER(BCD)
  FBLD Load BCD
  FBSTP Store BCD and pop

## Slide 4: II. Arithmetic Instructions
1. Addition
FADD Add real
FADDP Add real and pop
FIADD Add integer
2. Subtraction
FSUB Subtract real
FSUBP Subtract real and pop
FISUB Subtract integer
FSUBR Subtract real reversed
FSUBRP Subtract real and pop
FISUBR Subtract integer reversed

## Slide 5: II. Arithmetic Instructions
3. Multiplication
FMUL Multiply real
FMULP Multiply real and pop
FIMUL Multiply integer
4. Advanced
FABS Absolute value
FCHS Change sign
FPREM Partial remainder
FPRNDINT Round to integer
FSCALE Scale
FSQRT Square root
FXTRACT Extract exponent and mantissa.

## Slide 6: III. Compare Instructions.
FCOM Compare real
FCOMP Compare real and pop
FCOMPP Compare real and pop twice
FICOM Compare integer
FICOMP Compare integer and pop
FTST Test ST against +0.0
FXAM Examine ST

## Slide 7: IV. Transcendental
FPTAN Partial tangent
FPATAN Partial arctangent
F2XM1 2x - 1
FYL2X Y log2X
FYL2XP1 Y log2(X+1)

## Slide 8: Constant Instructions.
FLDZ Load +0.0
FLDI Load+1.0
FLDPI Load π
FLDL2T Load log210
FLDL2E Load log2e
FLDLG2 Load log102
FLDLN2 Load loge2

## Slide 9: Weblinks
http://www.psnacet.edu.in/courses/ECE/Microcontroller%20and%20Microprocessor/lecture5.pdf
http://www2.math.uni-wuppertal.de/~fpf/Uebungen/GdR-SS02/opcode_f.html