## Slide 1: MODULE-6 CO-PROCESSOR

## Slide 2: INSTRUCTION SET 8087
The 8087 co-processor has 68 additional instructions to the instruction set of 8086.
These instructions are fetched by 8086 but are executed by 8087.
The execution of 8087 instructions is transparent to the programmer.
When the 8086 comes across an 8087 instruction, it executes the ESCAPE instruction code to bypass the instruction opcode and control of the local bus to 8087 co-processor.

## Slide 3: 8087 INSTRUCTION TYPES
Data Transfer
Arithmetic
Comparison
Transcendental
Constant
Coprocessor control

## Slide 4: Data Transfer Instructions
Floating Point Data Transfer
Integer Data Transfer
BCD Data Transfer

## Slide 5: Floating Point Data Transfer Instructions
FLD(Load Real)
Loads 80-bit floating-point data to Top of Stack (ST). Stack pointer is then decremented by 1. Data can be retrieved from memory, or another stack register.
Examples :

## Slide 6
  FST (Store real)
This instruction stores current content of the top of the stack into memory or a specified co-processor register.
During copy, the data rounding occurs using the rounding control bits in floating point control register.
Examples :

## Slide 7
  FSTP (Store floating point number and pop)
This instruction stores a copy of the top of the stack into memory or any specified co-processor register and pop the data from the top of stack.
Examples
  FXCH Exchange
The FXCH instruction exchanges the contents of specified register with top of stack.
Examples:

## Slide 8: Integer Data Transfer Instructions
FILD (Load integer)
FIST (Store integer)
FISTP (Store integer and pop)

## Slide 9
FILD (Load integer)
loads the specified integer data operand to the top of the stack.
FIST (Store integer) and FISTP (Store integer and pop):
The instructions FIST and FISTP work in an exactly similar manner as FST/FSTP except that the operands are integer operands.

## Slide 10: BCD Data Transfer Instructions
The 8087 has two BCD data transfer instructions
FBLD (loads the top of stack with BCD memory data), and FBSTP (stores top of the stack and does a pop).
Both the instructions work in an exactly similar manner as FLD and FSTP except that the operands are BCD numbers.

## Slide 11: Arithmetic Instructions
1. Addition
FADD Add real
FADDP Add real and pop
FIADD Add integer
These two instructions perform real or integer addition of the specified operand with the stack top.
After addition, the results are stored in the destination operand.
The operand may be any of the stack registers or a memory location.

## Slide 12
2. Subtraction
FSUB Subtract real
FSUBP Subtract real and pop
FISUB Subtract integer
FSUBR Subtract real reversed
FSUBRP Subtract real and pop
FISUBR Subtract integer reversed
These instructions perform real or integer subtraction of the specified operand from the stack top.
The operand may be any of the stack register or memory.
After subtraction, the result of the operation is stored in the destination operand.

## Slide 13: Arithmetic Instructions
3. Multiplication
FMUL Multiply real
FMULP Multiply real and pop
FIMUL Multiply integer
These two instructions perform real or integer multiplication of the specified operand with stack top.
The specified operand may be a register or a memory location.
After multiplication, the result will be stored in the destination operand.

## Slide 14: Arithmetic Instructions
4. Division
FDIV Multiply real
FDIVP Multiply real and pop
FDIVR Multiply integer
FDIVRP
These four instructions perform real or integer division.
When the destination is not specified, the top of stack is the destination operand and source operand may be a memory operand of short real or long real type.
If both destination and source operands are specified then compute the division and store the result in the destination.

## Slide 15: Arithmetic Instructions
5. Advanced
FABS : This instructions replaces the content of stack top by its absolute value.
FCHS: This instruction changes the sign of the content of stack top.
FPREM: divides the stack top (ST) by ST(1)and then store the remainder to the stack top (ST).
FPRNDINT: rounds the content of ST(0) to its integer value.

## Slide 16
FSCAL: multiplies the content of stack top (ST) by 2n, where n is integer part of ST(1) and store result in ST.
FSQRT: finds out the square root of the content of the stack top and stores the result on stack top again.
FXTRACT: extracts the exponent and fraction of stack top and stores them in stack of registers.
Note:

## Slide 17: Comparison Instructions.
FCOM Compare real
FCOMP Compare real and pop
FCOMPP Compare real and pop twice
FICOM Compare integer
FICOMP Compare integer and pop
FIST Test ST is zero
FXAM Examine ST
The comparison instructions of the 8087 co-processor are used to compare the two values on the top of stack and set the condition code flags appropriately.

## Slide 18: Transcendental Instructions
FPTAN Partial tangent
used to compute the partial tangent of an angle , where must be in the range 0° . The value of angle must be stored at the stack top. The result is computed in the form of a ratio of ST/ST(1).
FPATAN Partial arc tangent
The FPATAN instruction calculates the are tangent (inverse tangent) of a ratio ST(1)/ST(0). The stack is popped and the result is stored on the top of stack. Its function can be expressed as

## Slide 19
F2XM1
Calculates the expression (2x-1). The value of x is stored at the top of the stack.
FYL2X
FYL2XP1

## Slide 20: Constant Instructions.
FLDZ Load +0.0
FLDI Load+1.0
FLDPI Load π
FLDL2T Load log210
FLDL2E Load log2e
FLDLG2 Load log102
FLDLN2 Load loge2
These instructions load the specific constants to the top of the register stack. Stack top is an implicit operand in all instructions

## Slide 21: CO-PROCESSOR CONTROL INSTRUCTIONS
used to program the numeric processor or to handle the internal functions like flags manipulations, exception handling, processor environment maintenance and preparation, etc.

## Slide 23: ALP Programming with 8087
Write a program to add three numbers and store the result.
Program
finit  Initialize the coprocessor to start at the beginning of the stack
fld X  Load X into ST(0); ST(0) = X
fld Y  ST(0) = Y, ST(1) = X
fld Z  ST(0) = Z, ST(1) = Y, ST(2) = Z
fadd ST(1)  Add Y and Z and store the result in ST(0)
fadd ST(2)  Add X and Y+Z and store the result in ST(0)
fst sum  Store the added result in the memory location named ‘sum’