## Slide 1: Networks and communication
Module 5
Routing protocols (Part 1)
Dr.S.L.JAYALAKSHMI,
VIT Chennai

## Slide 2: Outline
Routing
Routing Protocols
Classification of Routing Protocols
Distance Vector Routing
Example

## Slide 3: Routing -Introduction
What is Routing in Networks?
  A Routing is a process of selecting path along which the data can be transferred from source to the destination in a network or between or across multiple networks.
  Routing is performed by a special device known as a router. Networking device that forwards the packet based on the information available in the packet header and forwarding table.
  Router works at the network layer in the OSI model and internet layer in TCP/IP model.
  Routing algorithms (Software)- Used for routing the packets.
Notes: Routing is the process of selecting a path for traffic in a network or between or across multiple networks.
Packet forwarding is the transit of network packets from one network interface to another. Intermediate nodes are typically network hardware devices such as routers, gateways, firewalls, or switches.
  Routing algorithms (Software)- Used for routing the packets. The routing algorithm is nothing but a software responsible for deciding the optimal path through which packet can be transmitted.
  Routing is the decision over which interface a packet is to be sent. ... Routing tables contain network addresses and the associated interface or nexthop. This refers to ip route and ip rule (in a Linux context). Forwarding refers to packets which reach a system but are not destined for this system.
Static routing has three primary uses:
ease of routing table maintenance in smaller networks with little growth or change.
Routing to and from stub networks. A network accessed by a single route, and the router has only one neighbor.
Single default route to represent a path to any network.

## Slide 4: Routing -Introduction
Routing protocols - use the metric to determine the best path for the packet delivery. The metric is the standard of measurement such as hop count, bandwidth, delay, current load on the path, etc. used by the routing algorithm to determine the optimal path to the destination.
The routing algorithm initializes and maintains the routing table for the process of path determination.
Notes: The most common metric values are given below:
Hop count: Hop count is defined as a metric that specifies the number of passes through internetworking devices such as a router, a packet must travel in a route to move from source to the destination. If the routing protocol considers the hop as a primary metric value, then the path with the least hop count will be considered as the best path to move from source to the destination.
Delay: It is a time taken by the router to process, queue and transmit a datagram to an interface. The protocols use this metric to determine the delay values for all the links along the path end-to-end. The path having the lowest delay value will be considered as the best path.
Bandwidth: The capacity of the link is known as a bandwidth of the link. The bandwidth is measured in terms of bits per second. The link that has a higher transfer rate like gigabit is preferred over the link that has the lower capacity like 56 kb. The protocol will determine the bandwidth capacity for all the links along the path, and the overall higher bandwidth will be considered as the best route.
Load: Load refers to the degree to which the network resource such as a router or network link is busy. A Load can be calculated in a variety of ways such as CPU utilization, packets processed per second. If the traffic increases, then the load value will also be increased. The load value changes with respect to the change in the traffic.
Reliability: Reliability is a metric factor may be composed of a fixed value. It depends on the network links, and its value is measured dynamically. Some networks go down more often than others. After network failure, some network links repaired more easily than other network links. Any reliability factor can be considered for the assignment of reliability ratings, which are generally numeric values assigned by the system administrator.

## Slide 5: Types of routing
    Static routing table- It is created, maintained, and updated by a network administrator, manually.
    Default Routing- It is a technique in which a router is configured to send all the packets to the same hop device, and it doesn't matter whether it belongs to a particular network or not. A Packet is transmitted to the device for which it is configured in default routing.
    A dynamic routing table is created, maintained, and updated by a routing protocol running on the router.
Notes: Static Routing
A static route to every network must be configured on every router for full connectivity.
Static Routing is also known as Nonadaptive Routing.
It is a technique in which the administrator manually adds the routes in a routing table.
A Router can send the packets for the destination along the route defined by the administrator.
In this technique, routing decisions are not made based on the condition or topology of the networks
Advantages Of Static Routing
Following are the advantages of Static Routing:
No Overhead: It has ho overhead on the CPU usage of the router. Therefore, the cheaper router can be used to obtain static routing.
Bandwidth: It has not bandwidth usage between the routers.
Security: It provides security as the system administrator is allowed only to have control over the routing to a particular network.
Disadvantages of Static Routing:
Following are the disadvantages of Static Routing:
For a large network, it becomes a very difficult task to add each route manually to the routing table.
The system administrator should have a good knowledge of a topology as he has to add each route manually.
Default Routing
Default Routing is a technique in which a router is configured to send all the packets to the same hop device, and it doesn't matter whether it belongs to a particular network or not. A Packet is transmitted to the device for which it is configured in default routing.
Default Routing is used when networks deal with the single exit point.
It is also useful when the bulk of transmission networks have to transmit the data to the same hp device.
When a specific route is mentioned in the routing table, the router will choose the specific route rather than the default route. The default route is chosen only when a specific route is not mentioned in the routing table.
Dynamic Routing
It is also known as Adaptive Routing.
It is a technique in which a router adds a new route in the routing table for each packet in response to the changes in the condition or topology of the network.
Dynamic protocols are used to discover the new routes to reach the destination.
In Dynamic Routing, RIP and OSPF are the protocols used to discover the new routes.
If any route goes down, then the automatic adjustment will be made to reach the destination.
The Dynamic protocol should have the following features:
All the routers must have the same dynamic routing protocol in order to exchange the routes.
If the router discovers any change in the condition or topology, then router broadcast this information to all other routers.
Advantages of Dynamic Routing:
It is easier to configure.
It is more effective in selecting the best route in response to the changes in the condition or topology.
Disadvantages of Dynamic Routing:
It is more expensive in terms of CPU and bandwidth usage.
It is less secure as compared to default and static routing.

## Slide 6: Routing Protocols
  The purpose of any routing protocol is
  to dynamically communicate information about all network paths used to reach a destination
  to select the best path to reach a destination network.
Notes: Shortest Path routing
  Each link has a cost that reflects
    –The length of the link
    – Delay on the link
    – Congestion
    – $$ cost
  Cost may change with time . The length of the route is the sum of the costs along the route and the shortest path is the path with minimum length.
  Shortest Path algorithms
  – Bellman-Ford: centralized and distributed versions
  – Dijkstra’s algorithm

## Slide 7: Classification of Routing Protocol
Notes: Intradomain routing protocols ignores the internet outside the AS(autonomous system). Interdomain routing protocol assumes that the internet contains the collection of interconnected AS(autonomous systems).
Border Gateway Protocol (BGP) is a standardized exterior gateway protocol designed to exchange routing and reachability information between autonomous systems (AS) on the Internet.
Path Vector
Path vector (PV) protocols, such as BGP, are used across domains aka autonomous systems. In a path vector protocol, a router does not just receive the distance vector for a particular destination from its neighbor; instead, a node receives the distance as well as path information (aka BGP path attributes), that the node can use to calculate (via the BGP path selection process) how traffic is routed to the destination AS.
Distance Vector
The distance vector (DV) protocol is the oldest routing protocol in practice. With distance vector routes are advertised based upon the following characteristics:
Distance - How far the destination network is based upon a metric such as hop count.
Vector - The direction (next-hop router or egress interface) required to get to the destination.
This routing information is exchanged between directly connected neighbours.[2] Therefore when a node receives a routing update, it has no knowledge of where the neighbour learned it from. In other words, the node has no visibility of the network past its own neighbour. This part of distance vector is also known as "routing by rumour".
Furthermore, routing updates are sent in full (rather than delta-based updates) and at regular intervals, resulting in extremely slow convergence times - one of the key downfalls to distance vector protocols. In addition due to the slow convergence times and "routing by rumour", distance vector protocols are prone to routing loops.
However, on the flipside, the resource consumption is low compared to link-state, due to not having to hold the full state of the entire topology.
Link-state
In contrast to distance vector routing, link state routing (OSPF, ISIS) relies on each node advertising/flooding the state (i.e. delay, bandwidth etc) of their links to every node within the link state domain. This results in each node building a complete map of the network (shortest path tree), with itself as the root using the shortest path first algorithm, also known as the Dijkstra algorithm.
Unlike distance vector link-state neighbours only sends incremental routing updates (LSAs) rather than a full routing update. Also, these updates are only sent at the point a change in the network topology occurs, rather than at regular intervals.
Link-state protocols provide extremely low convergence times and, due to each router having a complete view of the network, aren't prone to the same routing loops seen with DV-based protocols.
However, due to the computation required for the algorithms to run across the shortest path trees upon each node, greater resources are consumed compared to that of distance vector, however, this really isn't a concern with the systems of today.
Hybrid
A hybrid routing protocol consists of characteristics from both, link state and distance vector routing protocols.
For example, EIGRP can be considered a hybrid routing protocol, as it displays characters of both. As shown below:
Distance VectorLink-stateEIGRP routers only advertise the best route , not every route that is aware of.An EIGRP router forms neighbour relationships.EIGRP routers do not have a complete network map of the topology, but only what it has been told by its neighbour aka "routing by rumour".Triggered updates are sent only when a topology change occurs.References
"

## Slide 8: Distance Vector Routing
Completely decentralized
No node has complete information about the costs of all network links
Gradual calculation of path by exchanging information with neighbors
A
C
D
B
E
Notes: The Distance vector algorithm is iterative, asynchronous and distributed.
  Distributed: It is distributed in that each node receives information from one or more of its directly attached neighbors, performs calculation and then distributes the result back to its neighbors.
  Iterative: It is iterative in that its process continues until no more information is available to be exchanged between neighbors.
  Asynchronous: It does not require that all of its nodes operate in the lock step with each other.
The Distance vector algorithm is a dynamic algorithm.
It is mainly used in ARPANET, and RIP.
Each router maintains a distance table known as Vector.
Three Keys to understand the working of Distance Vector Routing Algorithm:
Knowledge about the whole network: Each router shares its knowledge through the entire network. The Router sends its collected knowledge about the network to its neighbors.
Routing only to neighbors: The router sends its knowledge about the network to only those routers which have direct links. The router sends whatever it has about the network through the ports. The information is received by the router and uses the information to update its own routing table.
Information sharing at regular intervals: Within 30 seconds, the router sends the information to the neighboring routers.

## Slide 9: Specifics
Each node constructs a one-dimensional array (Vector) containing the “distances” or “costs” to all other nodes (as it relates to its knowledge) and distributes it to its immediate neighbors.
Key thing -- each node knows the cost of links to its neighbors.
If no link exists between two nodes, the cost of a direct link between the nodes is “infinity”.

## Slide 10: An Example
 | A | B | C | D | E
A | 0 | 1 | 1 | 1 | ∞
B | 1 | 0 | ∞ | 1 | 1
C | 1 | ∞ | 0 | 1 | ∞
D | 1 | 1 | 1 | 0 | 1
E | ∞ | 1 | ∞ | 1 | 0
Internal Information at each node(Router) ----->
A
C
D
B
E

## Slide 11: Routing Tables
With this information, routing table at A is -->
 | Cost | Next Hop
B | 1 | B
C | 1 | C
D | 1 | D
E | ∞ | -
A
C
D
B
E

## Slide 12: Evolution of the table.
  Each node sends a message to neighbors with a list of distances (From Node A to others).
  B --> A with E at distance 1.
 | Cost | Next Hop
B | 1 | B
C | 1 | C
D | 1 | D
E | 2 | B
A
C
D
B
E

## Slide 13: Final Distance Matrix
 | A | B | C | D | E
A | 0 | 1 | 1 | 1 | 2
B | 1 | 0 | 2 | 1 | 1
C | 1 | 2 | 0 | 1 | 2
D | 1 | 1 | 1 | 0 | 1
E | 2 | 1 | 2 | 1 | 0
A
C
D
B
E

## Slide 14: Convergence
In the absence of topological changes -- few exchanges between neighbors before complete routing table is formed.
This table is consistent.
Convergence is achieved.
Notice -- no centralized authority

## Slide 15: Routing updates
When are routing updates sent ?
  Periodic updates
    Even if nothing has changed, send periodically. Main reason is to let other nodes know that the sender is alive.
    Refresh information that might be needed if some of the routes were to become unavailable.
  Triggered updates
    When a node receives an update from one of its neighbors which may lead to a change in its routing tables (could be due to change in link cost).
  Note: typically order of periodicity is seconds to several minutes.

## Slide 16: Link/Node Failures
Nodes that first notice send new lists of distances to neighbors.
How do they detect failures ?
  Route updates don’t arrive
  Probing with test packets.

## Slide 17: Example
  Let link from B to E fail.
  B sets new distance to E to ∞; sends update to A and D .
  A was initially routing to E via B. So it now sets link cost to E to ∞.
  Next update from D; A learns that D has 1 hop path to E.
  A now can reach E in 2 hops via D.
  A sends an update to B. Thus, B now, can reach E via D in 2 hops.
A
C
D
B
E

## Slide 18: Count to Infinity
The process continues and thus, the system does not stabilize.
This is the count to infinity problem.
A
E
B
C
  For eg:
    A discovers that link to E is lost.
  If before A’s message (saying that link cost to E is ∞) is received, if B or C advertise that they can reach E in two hops, then A can be confused.
  Another possibility, B gets A’s update followed by C’s update which says that E is reachable in 2 hops.
  So B tells A this, and A thinks it can now reach E via B in 3 hops.
  This information reaches C who now thinks that it can reach E in 4 hops via A.

## Slide 19: Split Horizon
  One solution would be to approximate ∞ to say 10 hops.
  With Split Horizon, when a node sends a routing table update to its neighbors, it “does not” send those routes it learned from “a particular” neighbor, back to that neighbor.
    For example, B had E, 2, A. When it sends a route update to A, it does not include this.
  With split horizon with poison reverse, this update is reported but the link weight is set to ∞.
      For example B sends (E, ∞) to A.

## Slide 20: Does this work ?
Typically, in static networks where link failures/node failures are rare, this may be enough.
Speed of convergence is why, link state routing may be preferable -- it takes a while before routes converge.

## Slide 21: Purging routing entries
Each routing entry has a time-to-live (or TTL) field.
A counter -- initially set to MaxTTL.
This is then decremented and if TTL = 0, then, time to purge the entry.

## Slide 22: Routing Information Protocol (RIP)
Built based on distance vector routing.
In the Internet, goal of routers is to learn how to forward packets to various networks.

## Slide 23: An Example of RIP
  Routers advertise the cost of reaching networks.
  In this example, C’s update to A would indicate that C can reach Networks 2 and 3 with cost 0, Networks 5 and 6 with cost 1 and Network 4 with cost 2.
A
1
2
3
B
4
5
6
C
D

## Slide 24: Other RIP Details
Routing tables are exchanged every 30 seconds using the RIP advertisement.
If a router does not hear from its neighbor once every 180 seconds, the neighbor is deemed unreachable.
The router that detects this will modify its routing table and propagate the information.

## Slide 25: RIP implementation
RIP packets are sent using UDP.
Typically, there is a routing daemon (routed) that is an application layer process that provides access to routing tables.
Allows for the access of the tables.

## Slide 26: Thank You