## Slide 1: Network and Communication
Module 6 Congestion Control
Dr. S.L.JAYALAKSHMI
VIT Chennai

## Slide 2: Session Outline
Congestion – An introduction
Need for Congestion Control
Congestion control Mechanisms
  Additive Increase Multiplicative Decrease (AIMD)
  Slow Start
  Fast Retransmit

## Slide 3: What is Congestion?
Important issue to be considered in Packet Switched Networks
If the data (packets) sent on the network exceeds the capacity of the network, Congestion occurs
In otherwords, When too many packets are competing for the same link, the queue overflows and packet drop occurs leading to Network Congestion
Any system that involves waiting is prone to congestion
Congestion occurs in networks because the routers and switches have queues-buffers that hold the packets before and after processing

## Slide 4: Congestion – Example
A
B
C
10Mbps
10Mbps
10Mbps
10Mbps

## Slide 5: Congestion – Example
A
B
C
10Mbps
10Mbps
10Mbps
10Mbps

## Slide 6: Congestion – Example
A
B
C
10Mbps
10Mbps
10Mbps
10Mbps
Packet drop

## Slide 7: Why prevent congestion ?
Congestion is bad for the overall performance in the network.
  Excessive delays can be caused
  Retransmissions may result due to dropped packets
    Waste of capacity and resources
  Main reason for lost packets in the Internet is due to congestion -- errors are rare

## Slide 8: Congestion Control
Basic idea – to determine the capacity of the network to transmit the packet safely
In order to deal with congestion, a new state variable called “CongestionWindow” is maintained by the source.
MaxWindow=MIN(CongestionWindow,AdvertisedWindow)
Decrease window when TCP perceives high congestion.
Increase window when TCP knows that there is not much congestion
Some of the common Congestion control mechanisms are
  Additive Increase Multiplicative Decrease (AIMD)
  Slow start
  Fast retransmit, Fast recovery

## Slide 9: AIMD
Each time congestion occurs - the congestion window is halved
  Example, if current window is 16 segments and a time-out occurs (implies packet loss), reduce the window to 8 (half of 16)
Window is not allowed to fall below 1 segment
For each congestion window worth of packets that has been sent out successfully (an ACK is received), increase the congestion window by the size of a (one) segment

## Slide 10: AIMD
*Source - Computer Networks: A Systems Approach, Larry L. Peterson and Bruce S. Davie, Fifth Edition, The Morgan Kaufmann Series, Elsevier, 2011
Source
Destination
:
:

## Slide 11: More about AIMD
TCP source increments congestion window by a little for each ACK that arrives
  Increment = MSS * (MSS/Congestion Window)
    This is for each segment of MSS acked
  Congestion Window + = Increment
Thus, TCP demonstrates a sawtooth behavior !
*Source - Computer Networks: A Systems Approach, Larry L. Peterson and Bruce S. Davie, Fifth Edition, The Morgan Kaufmann Series, Elsevier, 2011

## Slide 12: TCP Slow Start
Additive Increase is good when source is operating at near close to the capacity of the network
  Too long to ramp up when it starts from scratch
  Slow start --> increase congestion window rapidly at cold start
Slow start allows for exponential growth in the beginning
    E.g. Initially CW =1, if ACK received, CW = 2
    If 2 ACKs are now received, CW = 4. If 4 ACKs are now received, CW =8 and so on
Note that upon experiencing packet loss, multiplicative decrease takes over

## Slide 13: TCP Slow Start
*Source - Computer Networks: A Systems Approach, Larry L. Peterson and Bruce S. Davie, Fifth Edition, The Morgan Kaufmann Series, Elsevier, 2011
Source
Destination
:
:

## Slide 14: Fast Retransmit
Fast Retransmit -- a heuristic that sometimes “triggers” the retransmission of a packet faster than permissible by the regular time-out.
Every time a data packet arrives at a receiver, the receiver ACKs even though the particular sequence number has been ACKed.
Thus, when a packet is received in out of order, resend the ACK sent last time -- a duplicate ACK!
Fig. Trace of TCP with Fast Retransmit
*Source - Computer Networks: A Systems Approach, Larry L. Peterson and Bruce S. Davie, Fifth Edition, The Morgan Kaufmann Series, Elsevier, 2011

## Slide 15: Duplicate ACKs
When a duplicate ACK is seen by the sender, it infers that the other side must have received a packet out of order.
  Delays on different paths could be different -- thus, the missing packets may be delivered.
  So wait for “some” number of duplicate ACKs before resending data.
  This number is usually 3.

## Slide 16: Duplicate ACKs
*Source - Computer Networks: A Systems Approach, Larry L. Peterson and Bruce S. Davie, Fifth Edition, The Morgan Kaufmann Series, Elsevier, 2011
Source
Destination
:
:
Packet 1
Packet 6
Packet 2
Packet 5
Packet 3
Packet 4
Retransmit packet 3
ACK 1
ACK 2
ACK 2
ACK 2
ACK 2
ACK 6

## Slide 17: References
Computer Networks: A Systems Approach, Larry L. Peterson and Bruce S. Davie, Fifth Edition, The Morgan Kaufmann Series, Elsevier, 2011.
Computer Networking: A Top Down Approach Featuring the Internet, J.F.Kurose and K.W. Ross, Sixth Edition, Pearson Education, 2012
Data Communication and Networking, Behrouz A. Fourozan, McGraw Hill Education, Fifth Edition, 2012